## Slide 1: Flexible and Scalable Systems for Network Management
Arpit Gupta
Adviser: Nick Feamster
Readers: Nick Feamster, Jennifer Rexford, and Walter Willinger
Examiners: Nick Feamster, Marshini Chetty, and Kyle Jamieson

## Slide 2: Making the ‘Net’ Work
Google
Cogent
Level3
Princeton
Outages
Congestion
Cyberattacks
Network Operator

## Slide 3: Monitor What’s Going On In the Network
jitter
distinct hosts
volume
delay
loss
asymmetry
…
Metrics
Is video streaming traffic jittery?
Receiving DNS responses from many distinct hosts?
Google
address
protocol
payload
device
location
…
Traffic
Flexible network monitoring is desired

## Slide 4: React to Various Network Events
Cogent
Level3
Google
Video Streaming Traffic
Other Traffic
Drop
Drop
Forward video streaming traffic via Level3, rest via Cogent
Drop the attack traffic before it reaches my network
Attack Traffic
Attack Traffic
address
protocol
payload
device
location
…
Traffic
forward
drop
rate-limit
modify
…
Actions
Flexible network control is desired

## Slide 5: Filling the “Flexibility” And “Scalability” Gap
Censorship Avoidance
Congestion Mgmt.
Traffic Scrubbing
Load Balance
DDoS Defense
Limitless Creativity
(Flexibility)
Limited Resources
(Scalability)
Traffic Engineering
Network Devices
Abstractions
Algorithms
Systems
Deployable
Gap

## Slide 6: Main Challenge
All Headers
add, subtract, bit operations
O(100 K)
O(ns)
Network devices need to process packets for millions of unique flows in 2-3 ns
Match | Destination Address
Actions | route, drop
State | O(1 M)
Speed | O(ns)
Routers
Programmable
Switches
CPUs
Headers + Payload
Any
O(1 B)
O(μs)
Flexible
Scalable
How to use programmable switches?

## Slide 7: Systems for Making the ‘Net’ Work
SDX
Sonata
Monitor
Control
[SIGCOMM’14]
[NSDI’16]
[SOSR’16]
[SOSR’17]
Flexible and scalable systems for network management
[SIGCOMM’18]
[SOSR’18]
[HotNets’16]

## Slide 8: Systems for Making the ‘Net’ Work
SDX
Sonata
Monitor
Control
[SIGCOMM’14]
[NSDI’16]
[SOSR’16]
[SOSR’17]
Flexible and scalable system for network control

## Slide 9: Flexible (Interdomain) Network Control
Cogent
Level3
Google
Video Streaming Traffic
Other Traffic
Drop
Drop
Forward video streaming traffic via Level3, rest via Cogent
Drop DNS responses to reflection attack victims
Attack Traffic
Attack Traffic

## Slide 10: Interdomain Traffic Control (Today)
Google
Cogent
Level3
Networks’ routers use Border Gateway Protocol (BGP) for exchanging traffic with each other
10/8 Traffic
I have routes for
IP prefix “10/8”
I have routes for
IP prefix “10/8”
How to enable flexible network control?
Inflexible

## Slide 11: Enabling Flexible Traffic Control
Google
Cogent
Level3
Replace all routers with programmable switches
How to enable incrementally deployable flexible traffic control?
Programmable Switches

## Slide 12: Rise of Internet Exchange Points (IXPs)
Google
Cogent
Level3
BGP Session
Switching Fabric
Route Server

## Slide 13: Software-Defined IXP (SDX)
Google
Cogent
Level3
Control Program
Programmable Switch
SDX Controller
Incrementally deployable

## Slide 14: Building SDX is Challenging
Programming abstraction
  How to let networks define flexible control programs for the shared SDX switch?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle programs for hundreds of peers, half million prefixes and matches on multiple header fields?

## Slide 15: Building SDX is Challenging
Programming abstraction
  How to let networks define flexible control programs for the shared SDX switch?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle programs for hundreds of peers, half million prefixes and matches on multiple header fields?

## Slide 16: Programming Abstraction
Google
Cogent
Level3
SDX Switch
drop? fwd?
How to express control programs for shared SDX switch without worrying about other’s programs?
Conflicting programs for DNS traffic
sPort=53  fwd(Level3)
sPort=53  drop

## Slide 17: Virtual Switch Abstraction
Google
Cogent
Level3
Virtual Switch
Virtual Switch
Virtual Switch
Google
Cogent
Level3
Participants express flexible control programs for their own virtual switches
SDX Switch
sPort=53  fwd(Level3)
sPort=53  drop

## Slide 18: Building SDX is Challenging
Programming abstraction
  How to let networks define flexible control programs for the shared SDX switch?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle programs for hundreds of peers, half million prefixes and matches on multiple header fields?

## Slide 19: Simple Example
Google
SDX
Level3
announces
10/8, 40/8
Cogent
announces
10/8, 40/8, 80/8
  dPort = 80 → fwd(Cogent)
Deliver HTTP traffic via Cogent

## Slide 20: Safe Interoperations with BGP
Google
  dPort = 80 → fwd(Cogent)
P
dPort = 80, dIP = 50.0.0.1
Cogent
announces:
10/8, 40/8, 80/8
SDX
How to enable flexibility w/o breaking global routing?
Ensure packet P is not forwarded to Cogent
Not announced by Cogent

## Slide 21: Naïve Solution: Program Augmentation
Google’s Program
dPort = 80 → fwd(Cogent)
BGP Prefix Announcements viewed by Google
 | Announcements
Level3 | 10/8, 40/8
Cogent | 10/8, 40/8, 80/8
dPort = 80, dIP ∈ 10/8 → fwd(Cogent)
dPort = 80, dIP ∈ 40/8 → fwd(Cogent)
dPort = 80, dIP ∈ 80/8 → fwd(Cogent)
Inflation by factor of three

## Slide 22: Building SDX is Challenging
Programming abstraction
  How to let networks define flexible control programs for the shared SDX switch?
Interoperation with BGP
  How to provide flexibility w/o breaking global routing?
Scalability
  How to handle programs for hundreds of peers, half million prefixes and matches on multiple header fields?

## Slide 23: Scalability Challenge
Destination Address
O (1 M)
How to compile programs for hundreds of peers, half million prefixes and matches on multiple header fields?
Match | All Headers
State | O(100 K)
Routers
Programmable Switch
How to make the best use of programmable switch and routers?

## Slide 24: Offload Complexity to the Packet
dPort = 80, dIP ∈ 10/8→ fwd(Cogent)
…
dPort = 80, Cogent ∈ Metadata→ fwd(Cogent)
Packet
dIP in 10/8
Reachable via
Cogent, Level3
Metadata
Google’s Program
dPort = 80 → fwd(Cogent)
BGP Prefix Announcements viewed by Google
 | Announcements
Level3 | 10/8, 40/8
Cogent | 10/8, 40/8, 80/8

## Slide 25: Reachability Attributes
Set of valid next hops for each prefix
Prefix | Attributes
10/8 | Level3, Cogent
40/8 | Level3, Cogent
80/8 | Cogent
Reachability Attributes
BGP Announcements
 | Announcements
Level3 | 10/8, 40/8
Cogent | 10/8, 40/8, 80/8

## Slide 26: Encoding Reachability Attributes (Strawman)
Level3
Cogent
Assign one bit for each SDX participant
Prefix | Attributes
10/8 | Level3, Cogent
40/8 | Level3, Cogent
80/8 | Cogent
Reachability Attributes
Reachability Bitmask
Prefix | Attributes
10/8 | 11
40/8 | 11
80/8 | 01

## Slide 27: Complexity at SDX’s Switch
dPort = 80 → fwd(Cogent)
Assign one bit for each SDX participant
dPort = 80, Metadata=*1→ fwd(Cogent)
Simplifies match rules at SDX
Level3
Cogent

## Slide 28: Metadata Size
Assign one bit for each SDX participant
100-1000 IXP participants. Strawman scales poorly!
Hierarchical Encoding
  Divide reachability attributes into clusters
  Trades metadata size with additional match rules
Only requires 33 bits for 500+ participants
Level3
Cogent

## Slide 29: SDX’s Performance
Chart: Number of TCAM Entries
| Baseline (Incorrect) | Naïve Augmentation | SDX
Number of Packet Tuples | 62000 | 68000000 | 65000
Log Scale
500+ participants, 96 M routes for 300K IP prefixes
3 orders of magnitude
reduction
68 M
Reduces metadata size to 33 bits at the cost of additional 3K TCAM entries
62 K
65 K

## Slide 30: SDX’s Performance
Chart: Number of TCAM Entries
| Baseline (Incorrect) | Naïve Augmentation | SDX
Number of Packet Tuples | 62000 | 68000000 | 65000
Log Scale
500+ participants, 96 M routes for 300K IP prefixes
Switch Constraint
(100 K)
SDX runs over commodity h/w switches
62 K
68 M
65 K

## Slide 31: How to Attach Metadata to the Packet?
Packet
dIP in 20/8
Metadata
Border routers can match on O(1M) IP prefixes
What’s the Next Hop MAC Address for “20/8”?
No changes required for border routers
Metadata
SDX Controller

## Slide 32: SDX: Contributions
Prototype with Quanta switches (5K lines of code)
Open-sourced with Open Networking Foundation
Used by DE-CIX, IX-BR, IIX, NSA; and Coursera assignment
Abstractions
Algorithms
System
Attribute encoding algorithms
Virtual switch abstraction
SDX [SIGCOMM’14] Internet-2 Innovation Award
iSDX [NSDI’16] Community Award
PathSets [SOSR’17]
Best Paper Award

## Slide 33: Systems for Making the ‘Net’ Work
SDX
Sonata
Monitor
Control
Flexible and scalable system for network monitoring
[SIGCOMM’18]
[SOSR’18]
[HotNets’16]

## Slide 34: Building Sonata is Challenging
Programming abstractions
  How to let network operators express queries for a wide-range of monitoring tasks?
Scalability
  How to execute multiple queries for high volume traffic in real time?

## Slide 35: Building Sonata is Challenging
Programming abstractions
  How to let network operators express queries for a wide-range of monitoring tasks?
Scalability
  How to execute multiple queries for high volume traffic in real time?

## Slide 36: Use Case: Detect DNS Reflection Attacks
👺
😵
Src: Victim
Dst: DNS
Src: Victim
Dst: DNS
Src: DNS
Dst: Victim
Src: DNS
Dst: Victim
DNS
DNS
Attacker
Victim
Identify hosts that receive
DNS responses from many distinct sources

## Slide 37: Packet as Tuple
Header
Metadata
Payload
Packet
traversed path, queue size, number of bytes, …
source/ destination address, protocol, ports, …
Packet = (path, qsize, nbytes,…
sIP, dIP, proto, sPort, dPort, …
payload)
Treat packet as a tuple

## Slide 38: Monitoring Tasks as Dataflow Queries
Detecting DNS Reflection Attack
Identify if DNS responses from unique sources to a single host exceeds a threshold (Th)
victimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
DNS responses
from unique sources
to a single host
exceeds a threshold
Express wide range of network monitoring tasks in fewer than 20 lines of code

## Slide 39: Building Sonata is Challenging
Programming abstractions
  How to let network operators express queries for a wide-range of monitoring tasks?
Scalability
  How to execute multiple queries for high volume traffic in real time?

## Slide 40: Where to Execute Monitoring Queries?
  Univmon [SIGCOMM’16]
  Marple [SIGCOMM’17]
  Gigascope [SIGMOD’03]
  NetQRE [SIGCOMM’17]
Match | Headers + Payload
Actions | Any
State | O(Gb)
Speed | O(μs)
Headers++
add, subtract, bit operations
O(Mb)
O(ns)
Switches
CPUs
Can we use both switches and CPUs?

## Slide 41: PISA* Processing Model
Programmable Deparser
Stages
ip.src=1.1.1.1
ip.dst=2.2.2.2
...
Packet Header Vector
Programmable Parser
Memory
Persistent State
ALU
  *RMT [SIGCOMM’13]

## Slide 42: Mapping Dataflow to Data plane
Which dataflow operators can be compiled to match-action tables?
 | Dataflow | Data plane
Model | Pipeline | Pipeline
Processing Unit | Operators | Match-Action Tables
Structured Data | Tuples | Packets

## Slide 43: Compiling Individual Operators
filter(p)
Stream of elements
Elements satisfying
predicate (p)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
Match | Action
p | 
udp.sport == 53 | 

## Slide 44: Compiling Individual Operators
reduce(f)
Match | Action
* | idx = hash(m.dstIP)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Stream of elements
Result of applying
function f over all elements
Memory
Match | Action
* | stateful[idx] += 1
1
2
3
4
5
6
7

## Slide 45: Compiling a Query
Programmable Deparser
Stages
Programmable Parser
State
Filter Map
Filter
D1
D2
Map
R1
R2

## Slide 46: Query Partitioning Decisions
Query Planner
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Resources?
Reduce Load?
Tuples
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)

## Slide 47: Query Partitioning ILP
Constraints
Goal: Minimize tuples sent to stream processor
Programmable Deparser
Stages
Programmable Parser
Memory
Persistent State
ALU
PHV Size
Number of
Actions
Total Stages
Stateful Memory
Packet Header Vector

## Slide 48: How Effective is Query Partitioning?
Chart: # Tuples at Stream Processor
| CPU-Only
Number of Packet Tuples | 1000000000 | 1
Log Scale
8 Tasks, 100 Gbps Workload
O(1 B)

## Slide 49: How Effective is Query Partitioning?
Chart: # Tuples at Stream Processor
| CPU-Only | Paritioning
Number of Packet Tuples | 1000000000 | 100000000
Log Scale
O(1 B)
O(100 M)
Only one order of magnitude reduction
8 Tasks, 100 Gbps Workload

## Slide 50: Query Partitioning Limitations
Filter Map
Filter
D1
D2
Map
R1
R2
distinct
reduce
How can we reduce the
memory footprint of stateful operators?

## Slide 51: Observations: Possible to Reduce Memory Footprint
Detecting DNS Reflection Attack
victim = pktStream
.map(dIP => dIP/8)
      .filter(p => p.udp.sPort == 53)
      .map(p => (p.dIP, p.sIP))
      .distinct()
      …
Only consider first 8 bits
Queries at coarser levels have smaller memory footprint

## Slide 52: Observations: Possible to Preserve Query Accuracy
Detecting DNS Reflection Attack
victim = pktStream
.map(dIP => dIP/8)
      .filter(p => p.udp.sPort == 53)
      .map(p => (p.dIP, p.sIP))
      .distinct()
      …
Hierarchical packet field
Query accuracy is preserved if refined with hierarchical packet fields

## Slide 53: Iterative Query Refinement
Filter
D1
D2
Map
R1
R2
Packet Stream
t+W
Map
Filter Map
Window
map(dIP=>dIP/8)
PISA Target
First, execute query at coarser level

## Slide 54: Iterative Query Refinement
Filter
D1
D2
Map
R1
R2
Filtered
Packet Stream
Map
Filter Map
Detection
Delay
Filter
Filter Map
Filter
D1
D2
Map
R1
R2
t+2W
Smaller
memory footprint
PISA Target
Then, execute query at finer level(s)
Smaller memory footprint at
the cost of additional detection delay

## Slide 55: Query Planning Problem
Goal
  Minimize tuples sent to the stream processor
Given
  Queries, packet traces
Determine
  Which packet field to use for iterative refinement?
  What levels to use for iterative refinement?
  What’s the partitioning plan for each refined query?
Augment partitioning ILP to compute both refinement and partitioning plans

## Slide 56: Sonata’s Performance
Chart: # Tuples at Stream Processor
| CPU-Only | Paritioning | Partitioning + Refinement
Number of Packet Tuples | 1000000000 | 100000000 | 100000
Log Scale
8 Tasks, 100 Gbps Workload
O(1 B)
O(100 M)
O(100 K)
Up to 4 orders of magnitude reduction

## Slide 57: Sonata: Contributions
Sonata [SIGCOMM’18]
Prototype with Barefoot switches and Apache Spark stream processor (9K lines of code)
Used by AT&T and Princeton course assignment
Abstractions
Algorithms
System
Query Planning Algorithms
(Partitioning and Refinement)
Dataflow queries over packet fields

## Slide 58: Summary
Flexible and scalable systems for nw. management
  SDX for programmatic control
    Flexible: match-action rules over virtual SDX switch
    Scalable: 3 orders of magnitude state reduction
  Sonata for network monitoring
    Flexible: dataflow queries over packet tuples
    Scalable: 4 orders of magnitude workload reduction
Programmable Switches

## Slide 59: Lessons Learned
Resource Pooling
  SDX: Router + Programmable switches
  Sonata: CPU + Programmable switches
Modular & Extensible Design
    SDX: OF 1.0  OF 1.3
    Sonata: fixed-function  PISA switches
Deployment Location Selection
  Minimize deployment threshold for operators

## Slide 60: Future Directions
Q1 Q2 Q3 …
Network-wide
Robust
Intelligent
Control
Monitor
Close the loop